## Slide 1: Multi Degree of Freedom System Free Vibration
Pertemuan – 6, 7
Mata Kuliah : Dinamika Struktur & Pengantar Rekayasa Kegempaan
Kode : CIV – 308
SKS : 3 SKS

## Slide 2
TIU :
Mahasiswa dapat menjelaskan tentang teori dinamika struktur.
Mahasiswa dapat membuat model matematik dari masalah teknis yang ada serta mencari solusinya.
TIK :
Mahasiswa mampu mendefinisikan derajat kebebasan, membangun persamaan gerak sistem MDOF

## Slide 3
Sub Pokok Bahasan :
Penentuan derajat kebebasan
Properti matrik kekakuan, massa dan redaman

## Slide 4
Structures cannot always be described by a SDoF model
In fact, structures are continuous systems and as such possess an infinite number of DoF
There are analytical methods to describe the dynamic behavior of continuous structures, which are rather complex and require considerable mathematical analysis.
For practical purposes to study Multi Degree of Freedom System (MDoF), we shall consider the multistory shear bulding model.

## Slide 5
A shear building may be defined as a structure in which there is no rotation of a horizontal section at the level of the floors
Assumption for shear building
The total mass of the structure is concentrated at the levels of the floors
The slabs/girders on the floors are infinitely rigid as compared to the columns
The deformation of the structure is independent of the axial forces present in the columns

## Slide 6
k1
k1
k2
k2
k3
k3
m2
m3
m1
u2
u3
u1
F1(t)
F2(t)
F3(t)
F3(t)
k3(u3 u2)
m3ü3
F2(t)
k2(u2 u1)
m2ü2
k3(u3 u2)
F1(t)
k1u1
m1ü1
k2(u2 u1)
Shear Building w/ 3 DoF
Free Body Diagram

## Slide 7
By equating to zero the sum of the forces acting on each mass :
Eq. (1) may conveniently be written in matrix notation as :
(2)
(1)

## Slide 8
Where :
And :

## Slide 9
Natural Frequencies and Normal Modes
EoM for MDoF system in free vibration is :
Solution of Eq. (3) is :
The substitution of Eq. (4) into Eq. (3) gives :
(3)
(4)
(5)

## Slide 10
The formulation of Eq (5) is known as an eigenvalue problem.
To indicate the formal solution to Eq. (5), it is rewritten as :
Eq (6) has non trivial solution if :
Eq.(7) gives a polynomial equation of degree n in wn2, known as characteristic equation of the system
(6)
A vibrating system with n DoF has n natural vibration frequencies wn, arranged in sequence from smallest to largest
(7)

## Slide 11
The n roots of Eq. (7) determine the n natural frequencies wn of vibration.
These roots of the characteristic equation are also known as eigenvalues
When a natural frequency wn is known, Eq.(6) can be solved for the corresponding vector fn
There are n independent vectors f, which are known as natural modes of vibration, or natural mode shape of vibration
These vectors are also known as eigenvector.

## Slide 12
Example 1
Determine :
The natural frequencies and corresponding modal shapes
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
u2
u1
3 m
W10x45
W10x21
W10x45
W10x21  I = 4,900 cm4
W10x45 I = 10,300 cm4
E = 2.106 kg/cm2

## Slide 13
Tugas 6
Determine :
The natural frequencies and corresponding modal shapes
W10x21  I = 4,900 cm4
W10x45 I = 10,300 cm4
E = 2.106 kg/cm2
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
u2
u1
3 m
W10x45
W10x21
W10x45
W3 = 20.000 kgf
W10x21
W10x21
u3
3 m

## Slide 14
Chart: 
| 1 | 0.85260000000000002 | 0.55459999999999998 | 0
mode 1 | 3 | 2 | 1 | 0
Chart: 
| 1 | -0.66200000000000003 | -1.004 | 0
mode 2 | 3 | 2 | 1 | 0
Chart: 
| 1 | -2.6574 | 5.3430999999999997 | 0
mode 3 | 3 | 2 | 1 | 0

## Slide 15
Modal & Spectral Matrices
The N eigenvalues, N natural frequencies, and n natural modes can be assembled compactly into matrices
Mode 1 2 n
DoF 1
2
…..
n
Modal matrix
Spectral matrix

## Slide 16
Orthogonality of Modes
The natural modes corresponding to different natural frequencies can be shown to satisfy the following orthogonality conditions :
When n ≠ r

## Slide 17
Free Vibration Response : Undamped System
EoM for MDoF Undamped Free Vibration is :
The differential equation (8) to be solved had led to the matrix eigenvalue problem of Eq.(6).
The general solution of Eq. (8) is given by a superposition of the response in individual modes given by Eq. (4).
Or
(8)
(9)
(10)

## Slide 18
Premultiply Eq. (10) with {fn}T[M] :
Regarding the orthogonality conditions :
From which :
  also
(11)
(11)

## Slide 19
If Eq. (8) is premultiplied by the transpose of the nth mode-shape vector {fn}T, and using Eq.(10) with its second derivative it becomes :
Eq.(11) is an EoM from SDoF Undamped System for mode n, which has solution :
Mn
Kn
(11)
Generalized mass
Generalized stiffness
(12)

## Slide 20
Solution for Eq. (8) becomes :
The procedure described above can be used to obtain an independent SDoF equation for each mode of vibration of the undamped structure.
This procedure is called the mode-superposition method
(13)

## Slide 21
Gaya pegas tiap lantai dari masing-masing mode dapat dicari dengan persamaan :

## Slide 22
Example 2
Based on data from Example 1, and the following initial condition, for each DoF plot the time history of displacement, regarding the 1st, and 2nd mode contribution
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
u2
u1
3 m
W10x45
W10x21
W10x45

## Slide 23
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
u2
u1
3 m
W10x45
W10x21
W10x45
Time History Displacement (cm)
Chart: Mode 1 Lantai 1
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | 0.55484 | 0.76283 | 0.93563 | 1.0653 | 1.1458 | 1.1734 | 1.1469 | 1.0675 | 0.93884 | 0.76687 | 0.55953 | 0.32638 | 0.078171 | -0.17364 | -0.41745 | -0.642 | -0.83693 | -0.99325 | -1.1037 | -1.1633 | -1.1692 | -1.1212 | -1.0215 | -0.87459 | -0.68737 | -0.46844 | -0.2279 | 0.023159 | 0.27315 | 0.51053 | 0.72436 | 0.90478 | 1.0435 | 1.134 | 1.1722 | 1.1564 | 1.0872 | 0.96782 | 0.80382 | 0.60273 | 0.37385 | 0.12771 | -0.12432 | -0.37061 | -0.5998 | -0.80133 | -0.96588 | -1.0859 | -1.1558 | -1.1724 | -1.1349
Chart: Mode 1 Lantai 2
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | 0.81486 | 1.1203 | 1.3741 | 1.5645 | 1.6827 | 1.7233 | 1.6844 | 1.5678 | 1.3788 | 1.1263 | 0.82176 | 0.47934 | 0.11481 | -0.25502 | -0.61309 | -0.94287 | -1.2291 | -1.4587 | -1.621 | -1.7085 | -1.7172 | -1.6467 | -1.5002 | -1.2845 | -1.0095 | -0.68797 | -0.3347 | 0.034013 | 0.40115 | 0.74979 | 1.0638 | 1.3288 | 1.5325 | 1.6654 | 1.7216 | 1.6983 | 1.5967 | 1.4214 | 1.1805 | 0.8852 | 0.54905 | 0.18756 | -0.18258 | -0.54429 | -0.8809 | -1.1769 | -1.4185 | -1.5948 | -1.6974 | -1.7218 | -1.6667
Chart: Mode 2 Lantai 1
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | 0.045149 | -0.16886 | -0.28877 | -0.24777 | -0.068704 | 0.14865 | 0.28317 | 0.2599 | 0.091802 | -0.12745 | -0.27568 | -0.27029 | -0.11429 | 0.1054 | 0.26636 | 0.27889 | 0.13602 | -0.082651 | -0.25526 | -0.28563 | -0.15684 | 0.059352 | 0.24247 | 0.29047 | 0.17662 | -0.035658 | -0.22806 | -0.29338 | -0.19522 | 0.011727 | 0.21214 | 0.29434 | 0.21252 | 0.012282 | -0.1948 | -0.29334 | -0.22841 | -0.03621 | 0.17617 | 0.29038 | 0.24278 | 0.059896 | -0.15637 | -0.2855 | -0.25554 | -0.083184 | 0.13552 | 0.27871 | 0.26659 | 0.10592 | -0.11378
Chart: Mode 2 Lantai 2
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | -0.014859 | 0.055573 | 0.095038 | 0.081544 | 0.022611 | -0.048921 | -0.093193 | -0.085535 | -0.030213 | 0.041944 | 0.090729 | 0.088956 | 0.037614 | -0.034688 | -0.087661 | -0.091785 | -0.044764 | 0.027201 | 0.084009 | 0.094004 | 0.051617 | -0.019533 | -0.079799 | -0.095598 | -0.058126 | 0.011735 | 0.075057 | 0.096555 | 0.064248 | -0.0038595 | -0.069817 | -0.09687 | -0.069943 | -0.0040422 | 0.064111 | 0.09654 | 0.075173 | 0.011917 | -0.05798 | -0.095568 | -0.079902 | -0.019712 | 0.051462 | 0.09396 | 0.0841 | 0.027377 | -0.044602 | -0.091727 | -0.087738 | -0.034859 | 0.037445

## Slide 24
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
fs2
fs1
3 m
W10x45
W10x21
W10x45
Chart: fs, mode 1 Lt 1
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | 759.5932 | 1044.3372 | 1280.9033 | 1458.3779 | 1568.5738 | 1606.4073 | 1570.1331 | 1461.4246 | 1285.2967 | 1049.8749 | 766.0195 | 446.8257 | 107.0187 | -237.7254 | -571.5026 | -878.9148 | -1145.7805 | -1359.7884 | -1511.0657 | -1592.6336 | -1600.7292 | -1534.979 | -1398.4163 | -1197.341 | -941.0293 | -641.3054 | -311.9965 | 31.7057 | 373.9451 | 698.9336 | 991.6784 | 1238.6745 | 1428.5273 | 1552.4785 | 1604.8098 | 1583.1071 | 1488.3716 | 1324.9736 | 1100.4512 | 825.1621 | 511.8061 | 174.8392 | -170.1935 | -507.3747 | -821.1494 | -1097.0424 | -1322.3259 | -1486.6072 | -1582.3074 | -1605.0117 | -1553.6726
Chart: fs, mode 1 Lt 2
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | 2308.0808 | 3173.2967 | 3892.1202 | 4431.3902 | 4766.2286 | 4881.1886 | 4770.9667 | 4440.6477 | 3905.4702 | 3190.1232 | 2327.6076 | 1357.7134 | 325.1843 | -722.3463 | -1736.5532 | -2670.6484 | -3481.5397 | -4131.8186 | -4591.4859 | -4839.3362 | -4863.9353 | -4664.1485 | -4249.1924 | -3638.2101 | -2859.3877 | -1948.6544 | -948.0246 | 96.34 | 1136.2602 | 2123.7618 | 3013.2888 | 3763.8049 | 4340.687 | 4717.3219 | 4876.3346 | 4810.3893 | 4522.5283 | 4026.0314 | 3343.8032 | 2507.3167 | 1555.1612 | 531.2621 | -517.1455 | -1541.6959 | -2495.1238 | -3333.4452 | -4017.9862 | -4517.167 | -4807.9592 | -4876.9478 | -4720.9502
Time History Spring Force (kg)
Chart: fs, mode 2 Lt 1
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | 781.0864 | -2921.2895 | -4995.8198 | -4286.503 | -1188.5955 | 2571.6394 | 4898.8661 | 4496.2717 | 1588.1961 | -2204.8784 | -4769.3169 | -4676.1237 | -1977.2294 | 1823.4469 | 4608.0342 | 4824.8623 | 2353.1069 | -1429.8827 | -4416.0912 | -4941.4979 | -2713.3275 | 1026.8047 | 4194.7651 | 5025.2544 | 3055.4946 | -616.8945 | -3945.5283 | -5075.5745 | -3377.3314 | 202.8798 | 3670.0393 | 5092.1234 | 3676.6966 | 212.4848 | -3370.1311 | -5074.791 | -3951.5983 | -626.4356 | 3047.7991 | 5023.6926 | 4200.2073 | 1036.2183 | -2705.1881 | -4939.1683 | -4420.8696 | -1439.1064 | 2344.5777 | 4821.7803 | 4612.1168 | 1832.4191 | -1968.3672
Chart: fs, Mode 2 Lt 2
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | -531.8548 | 1989.1549 | 3401.7374 | 2918.7517 | 809.3346 | -1751.0723 | -3335.7199 | -3061.5867 | -1081.4293 | 1501.3386 | 3247.5077 | 3184.0509 | 1346.3286 | -1241.6155 | -3137.6876 | -3285.3295 | -1602.2699 | 973.6311 | 3006.9905 | 3364.7486 | 1847.5501 | -699.1685 | -2856.2857 | -3421.7798 | -2080.5374 | 420.0538 | 2686.5763 | 3456.0436 | 2299.6815 | -138.1443 | -2498.9912 | -3467.312 | -2503.5243 | -144.6845 | 2294.7787 | 3455.5101 | 2690.7094 | 426.5505 | -2075.2974 | -3420.7164 | -2859.9915 | -705.5784 | 1842.0079 | 3363.1624 | 3010.2441 | 979.9116 | -1596.4622 | -3283.2309 | -3140.4676 | -1247.7249 | 1340.2942

## Slide 25
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
u2
u1
3 m
W10x45
W10x21
W10x45
Time History Base Shear (kg)
Chart: Base Shear Mode 1
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | 3067.674 | 4217.634 | 5173.0235 | 5889.7681 | 6334.8024 | 6487.5959 | 6341.0997 | 5902.0723 | 5190.7669 | 4239.998 | 3093.6271 | 1804.5391 | 432.203 | -960.0717 | -2308.0558 | -3549.5633 | -4627.3202 | -5491.6069 | -6102.5516 | -6431.9697 | -6464.6645 | -6199.1275 | -5647.6087 | -4835.5511 | -3800.417 | -2589.9598 | -1260.0211 | 128.0457 | 1510.2054 | 2822.6954 | 4004.9671 | 5002.4794 | 5769.2143 | 6269.8004 | 6481.1444 | 6393.4964 | 6010.8999 | 5351.005 | 4444.2544 | 3332.4788 | 2066.9673 | 706.1013 | -687.339 | -2049.0706 | -3316.2732 | -4430.4876 | -5340.3121 | -6003.7742 | -6390.2666 | -6481.9595 | -6274.6228
Chart: Base Shear Mode 2
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12000000000000001 | 0.14000000000000001 | 0.16 | 0.18 | 0.19999999999999998 | 0.21999999999999997 | 0.23999999999999996 | 0.25999999999999995 | 0.27999999999999997 | 0.3 | 0.32 | 0.34 | 0.36000000000000004 | 0.38000000000000006 | 0.40000000000000008 | 0.4200000000000001 | 0.44000000000000011 | 0.46000000000000013 | 0.48000000000000015 | 0.50000000000000011 | 0.52000000000000013 | 0.54000000000000015 | 0.56000000000000016 | 0.58000000000000018 | 0.6000000000000002 | 0.62000000000000022 | 0.64000000000000024 | 0.66000000000000025 | 0.68000000000000027 | 0.70000000000000029 | 0.72000000000000031 | 0.74000000000000032 | 0.76000000000000034 | 0.78000000000000036 | 0.80000000000000038 | 0.8200000000000004 | 0.84000000000000041 | 0.86000000000000043 | 0.88000000000000045 | 0.90000000000000047 | 0.92000000000000048 | 0.9400000000000005 | 0.96000000000000052 | 0.98000000000000054 | 1.0000000000000004
 | 249.2316 | -932.1346 | -1594.0825 | -1367.7514 | -379.2609 | 820.5671 | 1563.1461 | 1434.685 | 506.7668 | -703.5398 | -1521.8092 | -1492.0728 | -630.9008 | 581.8314 | 1470.3466 | 1539.5328 | 750.837 | -456.2516 | -1409.1008 | -1576.7492 | -865.7774 | 327.6362 | 1338.4793 | 1603.4745 | 974.9572 | -196.8407 | -1258.952 | -1619.5308 | -1077.6499 | 64.7356 | 1171.0481 | 1624.8113 | 1173.1723 | 67.8003 | -1075.3524 | -1619.2808 | -1260.8889 | -199.8851 | 972.5017 | 1602.9762 | 1340.2158 | 330.6399 | -863.1802 | -1576.0059 | -1410.6255 | -459.1948 | 748.1155 | 1538.5494 | 1471.6493 | 584.6943 | -628.073
Base Shear
(Gaya Geser Dasar)

## Slide 26
Assignment 7
Based on data from Assignment 6, and the following initial condition, for each DoF plot the time history of displacement, regarding the 1st, 2nd , and 3rd mode contribution.
Also plot the time history of spring force and base shear
Make a conclusion !!
Submit at the first meeting after Mid Test
W1 = 11.600 kgf
4,5 m
W10x21
W2 = 24.000 kgf
u2
u1
3 m
W10x45
W10x21
W10x45
W10x21  I = 4,900 cm4
W10x45 I = 10,300 cm4
E = 2.106 kg/cm2
W3 = 20.000 kgf
W10x21
W10x21
u3
3 m

## Slide 27
Free Vibration Response : Damped System
EoM for MDoF Damped Free Vibration is :
Using Eq. (10) and its derivative :
Premultiply Eq. (15) with {f}T :
(14)
(15)
(16)
Mn
Cn
Kn

## Slide 28
Eq.(16) is an EoM from SDoF Damped System for mode n, which has solution :
The displacement response of the system is then obtained by substituting Eq. (17) in Eq. (10)
(17)
(18)